User Manual

Access 7 AH Configuration tool

- Connect USB-RS232 adapter D9 connector to 7 AH Configuration tool

- Connect USB-RS232 adapter USB connector to PC and wait until device is installed

- Connect reader cable wires to 7 AH Configuration tool connector as follows:

red……………… +24V

black…………... GND

pink…………….. TX

grey…………….. RX

- Plug power adapter to wall socket. Reader starts up.

- Open Idesco 7 AH CONF SW.

- Refer to Access 7 AH CONF SW User manual for more instructions on creating and sending configuration files to reader.

- After successful reader configuration, unplug the power adapter from the wall socket.

- Remove reader cable wires

- If more readers will be configured, continue from section 3.